## Slide 1: Optimizing parallel reduction in CUDA
Follows the presentation of Mark Harris - Nvidia

## Slide 2: Parallel Reduction
Tree based approach in each thread block
Use multiple thread blocks
  To process large arrays
  To keep all the SMs on the GPU busy
  Each block process a portion of the array

## Slide 3: Parallel Reduction
CUDA has no global synchronization
Decompose the process into multiple kernel launches

## Slide 4: Optimization Goal
We should strive to reach peak GPU performance
  GFLOP/s for compute-bounded kernels
  Memory bandwidth for memory-bounded kernels
Reduction has very low computational need
  1 flop/element
We should strive for peak bandwidth

## Slide 5: Reduction v0
// Reduction in the global memory
__global__ void reduceKernel_v0(unsigned int *g_idata, unsigned int *g_odata, size_t dataSize)
{
unsigned int lid = threadIdx.x; // local id in the block
  unsigned int id = blockIdx.x * blockDim.x + threadIdx.x; // global id, base index of the thread block
  if (id >= dataSize) return;
  // do reduction in global memory
  for (unsigned int s = 1; s < blockDim.x; s *= 2)
  {
    // modulo arithmetic is slow!
    if ((lid % (2 * s)) == 0)
    {
    if (id + s < dataSize)g_idata[id] += g_idata[id + s];
    }
  __syncthreads();
  }
  // write result for this block to global memory
  if (lid == 0) g_odata[blockIdx.x] = g_idata[id];
}

## Slide 6: Reduction v1
V0 uses global memory to store intermediate results
Use shared memory instead

## Slide 7: Reduction v2
V1 : highly divergent branches

## Slide 8: Reduction v2
Strided index and non-divergent branch

## Slide 9: Reduction v3
V2 memory access pattern
Notes: Bank conflict
Shared memory is divided into equally sized memory modules called banks
A bank can serve one request at once
Banks can be access simultaneously
If same bank is accessed, the request are serialized

## Slide 10: Reduction v3
Use sequential addressing instead
Notes: Bank conflict
Shared memory is divided into equally sized memory modules called banks
A bank can serve one request at once
Banks can be access simultaneously
If same bank is accessed, the request are serialized

## Slide 11: Reduction v4
In v3 half of the threads are idle in the first iteration
Halve the number of blocks
Replace the single shared memory load with two global memory reads and the first add of the reduction

## Slide 12: Reduction v5
V4 is still limited by address arithmetic and loop overhead
Unroll the loops

## Slide 13: Reduction v5
When s <= 32, only 32 active thread remained
These threads are in a single warp
Instructions are SIMD synchronous within a warp
  We do not need __synchthreads()
  If(tid < s) is also needless
Unroll the last 6 iterations of the loop
  Note: This saves useless work in all warps, not just the last one!
  Without unrolling, all warps execute every iteration of the for loop and if statement

## Slide 14: Reduction v6
Complete unrolling
If we know the number of iterations at compile time, we can unroll the whole reduction
  Block size is limited to 1024 threads
  We use power of 2 block sizes
  Loop can be unrolled for a fixed block size
Use templates
  generic solution

## Slide 15: Reduction v7
Algorithm cascading
Combine sequential and parallel reduction
  Each thread loads and sums multiple elements into shared memory
  Tree-based reduction in shared memory
  Each thread should sum O(log n) elements
    Or even more, try different parametrization