## Slide 1: Hierarchical Volumetric Fusion of Depth Images
László Szirmay-Kalos, Milán Magdics
Balázs Tóth, Tamás Umenhoffer
Notes: In this talk we present algorithms for on-line and real-time reconstruction of the 3D geometry based on the images of RGB and depth cameras.

## Slide 2: Real-time color & 3D information
Affordable integrated depth and color cameras

## Slide 3: Application: 3D scanning

## Slide 4: Application: limitations of compositing
Chroma keying
Augmented reality
Compositing can be based on color:
Fixed order
No shadows
No reflections, refractions, cross illumination

## Slide 5: Deph compositing (Zinemath)
Zinemath - ZLense

## Slide 6: 3D reconstruction of a point
t
f
(xc,yc,zc)
xi = fxc/zc
yi = fyc/zc
(cx, cy)
(cx,cy)
(X,Y)
xi =(X-cx)sx
yi =(Y-cy)sy
(xi,yi)
zc
Back projection

## Slide 7: 3D point cloud
http://through-the-interface.typepad.com/through_the_interface/2012/11/updated-autocad-integration-samples-for-kinect-sdk-v16.html

## Slide 8: Dynamic camera, static scene
Fusion
Point cloud
Object
Projection
Problems:
in different images the camera changes
camera tracking based on static objects
in different frames different points are visible
We need to maintain surface information
between points
Solution (Curless/Levoy):
Scene is represented by an emerging
distance field

## Slide 9: 3D reconstruction input
Depth image: distance of the visible surface in each pixel
  Noisy and unreliable

## Slide 10: Surface reconstruction
Curless-Levoy algorithm
Truncated Signed Distance Field (TSDF)
d(x,y,z)
voxel
d

## Slide 11: Aims
Reconstruct static scenes with moving camera
Real-time reconstruction
  GPU-based implementation
Fast camera tracking
  Common methods (SIFT, SURF etc.) are slow
Efficient, high resolution TSDF storage
  To reconstruct fine geometric details
  GPU memory is limited

## Slide 12: Proposed method
Two-level, hierarchical TSDF
  Observation: usually most of the scanned 3D space is empty
Iterative reconstruction algorithm
Camera tracking
Macrocell marking
Distance fusion
Distance generation
Macrocell refinement
Applications
Measured depth image
Camera pose
Divided cells
TSDF
3D mesh, etc.
Depths and normal vectors
Intersected
macro-cells

## Slide 13: Hierarchical TSDF
Macro-cell array
Decomposed
macro-cell
Micro-cell store
Micro cell block
88 8
Empty list
Empty
macro-cell

## Slide 14: Macro-cell marking
empty
intersected
not affected
visible surface
Truncation distance
macro-cells

## Slide 15: Macro-cell marking: gather-style
Wasteful!
macro-cells
Project each voxel
to the depth map
and compare depth

## Slide 16: Scatter-style marking (but still faster)
empty
intersected
not affected
visible surface
DDA steps
Truncation distance
macro-cells
Visit affected voxels
by ray-casting

## Slide 17: Avoiding atomic operations
Macro-cell marking
  Determine empty and intersected cells
  Without synchronization!
Index to the block of child micro-cells
0
31
Empty counter
is intersected
is empty
20
24

## Slide 18: Fusion
Distance fusion
  Only for the previously marked micro-cells
1
0.9
0.5
-0.1
-0.8
-1
0.5

## Slide 19: Rendering
Distance map generation
  Hierarchical DDA
    Different step size in the macro and micro cells
ray

## Slide 20: Camera tracking
Iterative Closest Point (ICP)
Back projection
of current depth
Zero-crossings
of the TSDF
q1
q2
qn
R, t
p1
p2
pn
Projective matching

## Slide 21: Results
Kinect2 depth camera
NVIDIA 690GTX GPU
Real-time reconstruction
1mm cell resolution

## Slide 22: Results
With the same memory usage: 8mm vs 1mm cell size
Kinect Fusion
Proposed method

## Slide 23: Thank you!

## Slide 24: Time of flight depth sensors
Pulsed modulation:
Accurate time measurement
expensive
Continuous modulation
Periodic distance